## Slide 1: Unified Symbol Driver
By lookwhoistalkinguvm@gmail.com

## Slide 2: Sequenced Symbol Driver Construction Pattern
Frame sequencing bus symbols
Sequencer
Driver
Frame
Bus Symbol 1
Bus Symbol 2
Bus Symbol n
...
(1)
(2)
(n)
sda
scl
sda
scl
sda
scl
Bus

## Slide 3: Procedural code :WB Write – Master Driver
always @(posedge clk) begin
if (ack_i==0) begin
m_vif.we_o <= ‘b1;
m_vif.stb_o <= ‘b1;
m_vif.addr_o <= VALID;
m_vif.dat_o <= VALID
etc ..
end else begin
m_vif. we_o<= ‘b0;
m_vif. stb_o<= ‘b0;
etc ..
end

## Slide 4: Procedural Code WB Write - Monitor
always @(posedge clk) begin
if (vif.stb_o==‘b1&&vif.we_o==‘b1&&vif.ack_i==1) begin
item.data = vif.wb_data_o;
item.addr = vif.wb_addr_o;
etc ..
end else begin
vif.ack_i <= ‘b0 ;
etc ..
end

## Slide 5: A possible solution ?
Use constraint coding instead of procedural coding.
Stimulus is created by the driver through constrained randomization.
Waves on the bus are checked by the monitor by using the same constraints in constraint checking mode.

## Slide 6: Item and Symbol Structures
symbol
Item
A
B
C
D
symbol extends uvm_object
phase FSM
rand sig1;
constraint c_symbol_wave {
(next_phase==A) -> sig1== 1 ;
(next_phase==B) -> sig1== 0 ;
}
randomize()
Done
Timer

## Slide 7: Symbol Timer
rand int unsigned next_timer;
int unsigned timer;
constraint c_next_timer {
next_timer==timer+1;
}
function void post_randomize;
timer = next_timer;
endfunction

## Slide 8: Symbol Phasing
// Symbol Phasing
rand symbol_phase next_phase;
symbol_phase phase;
constraint c_next_phase_sequencing {
(phase==A)-> next_phase inside {A, B};
(phase==B)-> next_phase inside {B, C};
(phase==C)-> next_phase inside {C, D};
(phase==D)-> next_phase inside {D, E};
}
constraint c_next_phase_timing {
if(timer >=0)
next_phase==A;
}
function void post_randomize;
phase = next_phase;
endfunction

## Slide 9: Constraint code WB Write Driver / Monitor
constraint c_done {
if(wb_ack_o==1)
m_done==1;
else
m_done==0;
}
constraint c_output_wave {
wb_cyc_i==1;
wb_stb_i==1;
wb_we_i==1;
}

## Slide 10: I2C Slave Start Bit
constraint c_done_monitoring {
if(next_phase==D)
m_done==1;
else
m_done==0;
}
constraint c_next_phase_sequencing {
(phase==A)-> next_phase inside {B};
(phase==B)-> next_phase inside {B, C};
(phase==C)-> next_phase inside {C, D};
(phase==D)-> next_phase inside {D};
}
constraint c_check_DUT_outputs {
(next_phase==A) -> scl_pad_o==1 &&sda_pad_o==1;
(next_phase==B) -> scl_pad_o==1 &&sda_pad_o==1;
(next_phase==C) -> scl_pad_o==1 &&sda_pad_o==0;
(next_phase==D) -> scl_pad_o==0 &&sda_pad_o==0;
}
constraint c_inactive {
scl_pad_i==1;
sda_pad_i==1;
}

## Slide 11: Symbol Use – Driver Side
constrant1
constraint2
rand in_sig_n
rand in_sig_1
symbol
randomize()
3
4
in_sig_1;
in_sig_2;
symbol
VIF
in_sig_1;
in_sig_n;
in_sig_2;
in_sig_n;
5
2
out_sig_1;
out_sig_2;
symbol
out_sig_n;
VIF
out_sig_1;
out_sig_2;
out_sig_n;
1

## Slide 12: Symbol Use – Monitor Side
monitor symbol queue
randomize()
3
2
out_sig_1;
out_sig_2;
symbol
out_sig_n;
VIF
out_sig_1;
out_sig_2;
out_sig_n;
1
in_sig_1;
in_sig_2;
in_sig_n;
in_sig_1;
in_sig_2;
in_sig_n;
constraint1
constraint2
rand in_sig_1
rand in_sig_n
monitor symbol queue
4
symbol
symbol
symbol
symbol
symbol
symbol
symbol
symbol
FAILED randomization
create new symbol to replace failed symbol

## Slide 13: GitHub Repository
https://github.com/lookwhoistalkinguvm/symbol_gen

## Slide 14: WB Symbol Example
agents\wb_agent\symbols\wb_write_symbol.svh
agents\wb_agent\symbols\ monitor_wb_write_symbol.svh
agents\wb_agent\agent\wb_agent_monitor.svh
agents\wb_agent\agent\wb_agent_driver.svh

## Slide 15: I2C Example
agents\symbol_gen_agent\symbols\symbol_gen_slave_start_symbol.svh
agents\symbol_gen_agent\symbols\monitor_symbol_gen_start_symbol.svh
agents\symbol_gen_agent\agent\symbol_gen_agent_driver.svh
agents\symbol_gen_agent\agent\symbol_gen_agent_monitor.svh

## Slide 16: Simulation and Docs Directories
tb\run\compile
tb\run\simulate
docs\SymbolDriver.pptx